## Slide 1
ADMIN GUIDE
Connecting a smart room
Turn any existing room into a smart room with a Wokwi simulation or a real ESP32: five steps, about six minutes, no SQL and no redeploy.
1
Open Smart room
2
Choose room + device
3
Copy ID + key
4
Paste into sketch
5
Check it's live
~1 min
in the web app
~5 min
on the device
0
SQL scripts or redeploys
Notes: This guide shows how an administrator adds a new smart room. Everything on the web side is in the admin console; the only device work is pasting two lines into the firmware.

## Slide 2
STEP 1 OF 5 · WEB APP
Open Admin → Smart room
1
2
3
4
1
Smart room tab
Admin console, third tab.
2
Connect a room
Opens the setup window (next step).
3
Device type
Badge shows Simulated (Wokwi) or Physical (ESP32).
4
Live status
Online = device reported in the last 30 s.
Notes: The Smart room tab lists only rooms that already have a device. Each card shows the device type and whether it is online. The Connect a room button starts the setup.

## Slide 3
STEP 2 OF 5 · WEB APP
Choose the room and the device
1
2
3
1
Room
Any existing room that has no device yet. Rooms are created in the Facilities tab.
2
Device
Simulated (Wokwi) or Physical (ESP32). Same firmware; both talk HTTPS + MQTT.
3
Connect
The browser makes a random 32-character key and saves only its SHA-256 hash.
Only admins can write device records (row-level security on room_devices).
Notes: Pick the room and say whether the device is simulated in Wokwi or a physical ESP32. The label only affects how it is shown; both run the same firmware and use HTTPS for status and MQTT for commands. On Connect, the key is generated in the browser and only its hash reaches the database.

## Slide 4
STEP 3 OF 5 · WEB APP
Copy the device ID and key
1
2
3
4
1
Shown once
Only the hash is stored, so copy it now. Lost it? Generate a new key later.
2
Two lines for sketch.ino
DEVICE_ID and DEVICE_KEY, ready to paste. The copy button copies both.
3
Live server address
API_BASE is always the deployed site, never localhost, so Wokwi can reach it.
4
Technical details
Status URL and MQTT topic, for anyone writing their own firmware.
Notes: The result window walks through the device steps. The key is shown only once because the database keeps just its SHA-256. The two sketch lines and the server address each have a copy button.

## Slide 5
STEP 4 OF 5 · DEVICE
Paste into the firmware and run it
1
2
3
4
5
1
Copy the project
Duplicate firmware/door-wokwi, one copy per room.
2
Paste lines 80–81
Replace DEVICE_ID and DEVICE_KEY (green).
3
Check the amber lines
API_BASE = live site. Real ESP32: set WIFI_SSID / WIFI_PASS.
4
Watch the Serial Monitor
"MQTT connected, listening on campus/rooms/…/cmd"
5
Build and start
PlatformIO build, then start the Wokwi simulation (or flash the board).
Illustration of the VS Code + Wokwi workspace. The serial lines are the firmware's real messages; MQTT settings stay unchanged.
Notes: On the device side you copy the firmware folder, paste the two lines, and check that API_BASE points at the live site. For a physical board you also set the Wi-Fi. After building, the serial monitor shows Wi-Fi and MQTT connecting.

## Slide 6
STEP 5 OF 5 · CHECK
Confirm it's live, and fix it if not
1
2
1 New room shows Online within ~10 s. Book it as a student and try the door code.
2 ⋯ menu: new key, or disconnect (history kept).
What you see | Likely cause | Fix
Card says "Never connected" | Device can't reach the site | Check API_BASE and Wi-Fi; read the Serial Monitor
OLED: "Device not registered" | ID or key pasted wrong, or an old key | Paste again, or ⋯ → New device key
OLED: "Server unreachable" | Wrong URL or site down | Open the live site; check API_BASE
Serial: "MQTT connect failed" | Broker settings | Commands still arrive via the 5 s status poll
Notes: Within about ten seconds the new room shows Online. If not, the table maps what you see to the usual cause. Remote commands fall back to the five-second status poll if MQTT is down.

## Slide 7
BEHIND THE SCENES
What happens after you click Connect
Admin browser
Campus Reserve
(Vercel + Supabase)
MQTT broker
(EMQX, TLS)
Device
(Wokwi / ESP32)
Connect: save SHA-256(key) only
HTTPS GET /api/room/status every 5 s (x-device-key)
booking, lock state, display text, pending commands
POST /api/room/event: door, presence, lights, AC
Remote command
publish, HMAC-signed
check signature + 60 s expiry
Notes: The browser saves only the key's hash. The device proves itself on every request with the key, which the server hashes and compares. Status and events go over HTTPS; remote commands go through the MQTT broker, signed with a key derived from the device key, and expire after 60 seconds. If MQTT is unavailable the same commands are picked up by the status poll.